## Slide 1: In-network data collection and processing with TinyOS
ARIANNA CASAROLI, MICHELE SCUTTARI

## Slide 2: Structure
TemperatureMonitoringC.nc
TemperatureMonitoringAppC.nc
TemperatureMonitoring.h
Contains the structure of the messages and some global parameters such as maximum temperature
includes
includes

## Slide 3: Structure
TemperatureMonitoringAppC
configuration
TemperatureMonitoringC
component
PoolC
component
DemoSensorC
component
AMSenderC
component
AMReceiverC
component
ActiveMessageC
component
TimerMilliC
component

## Slide 4: Components
DemoSensor  used to simulate the presence of the temperature sensor
TimerMilliC  used to build the timer for the sampling of the temperature and the selection of the new threshold
PoolC used to manage outgoing messages when the AMSenderC is still busy
AMSenderC  used to send messages
AMReceiverC  used to receive messages
ActiveMessageC

## Slide 5: The need of a queue
We decided to use a queue of messages in order to minimize the number of messages lost.
The problem is that when we need to send a message but the previous message has not finished the sending process yet, this message is discarded. This is caused by the fact that functions are synchronous, so if we call the send function (used to send a message) after the sendDone function (called when a message has been sent), the sendDone will be processed only after the send function and we are not able to be notified when the send process is actually free.
This problem is resolved by inserting a queue of messages and appending the outgoing message anytime the send process is busy. The messages in this queue are processed in the sendDone function.

## Slide 6: Messages
DATA message
Sent by the node "node_id" to the sink node
Contains the temperature measured by the node "sender"
node_id
temperature
sender
SETUP message
Message sent by the node "node_id"
Contains the new threshold
progressiveNum
node_id
threshold

## Slide 7: Is a tree network needed?
Not really. Thanks to the progressiveNum field in the SETUP message, a node can understand whether the message has already been received or not.
If the message has progressive number < than the current one
 the message is discarded

## Slide 8: TOSSIM – simulation
The TOSSIM simulation is in the python file simulation.py
It takes from arguments the number of nodes in the network, the topology file and the noise file
Then builds the network and the noise model
Eventually prints out the DEBUG messages returned by the nodes
We tried to build 4 different topologies in order to test the application from different points of view.

## Slide 9
Thank you for the attention